CNC Machinery

Module 3: Introduction to CNC

PREPARED BY

IAT Curriculum Unit

August 2008

© Institute of Applied Technology, 2008

Module 3: Introduction to CNC

Module Objectives:

- Define the term CNC.

- Recognize the advantages and disadvantages of CNC.

- Demonstrate familiarity with the MTS Simulator and TOPCAM software.

- Create a setup form.

- Create a setup sheet.

Module Contents

|  | Title | Page No. |
| --- | --- | --- |
| 1 | What is CNC? | 3 |
| 2 | Advantages of CNC machines. | 3 |
| 3 | Disadvantages of CNC machines | 3 |
| 4 | Starting with MTS | 4 |
| 5 | Preparing a setup form | 9 |
| 6 | Preparing a setup sheet | 13 |

| 1. What is CNC? CNC stands for Computer Numerical Control. It is the technology of controlling a machining operation using a computer program, which is called Numerical Control (NC) Program. Fig. 3.1 A simulator is used to create NC programs, simulating them and checking their quality. These programs can be transferred and executed on the real CNC machine to produce work parts. The used simulator in our study will be the MTS Simulator. Fig. 3.2 2. Advantages of CNC Increased productivity where productivity is the speed at which parts are produced. Constant quality of the work part which means producing the same quality for all work parts. Less scrap Better dimensional accuracy which gives exact and correct dimensions. Increased ability to produce difficult parts 3. Disadvantages of CNC High initial cost Need high qualified operator. | Fig. 3.1: CNC milling machine Fig. 3.2: MTS Simulator |
| --- | --- |
| 4. Starting with MTS: To start the MTS simulator: Click on the windows “start” button in the task bar. Point on “all programs”. Point on “TOPCAM V.7.1.3 English”. Click on “TOPCAM”. The start-up menu (Fig. 3.3) will offer you the following software modules for selection: TOPCAM: a CAD system for turning and milling. TOPTURN: used for turning programming, simulation and collision detection. TOPMILL used for milling programming, simulation and collision detection. Fig. 3.3 The start-up menu Let's select TOPTURN, and then choose the controller (Fig. 3.4). The controller is the link between the software (NC program) and the hardware (CNC machine). Fig. 3.4 choosing controller From the controllers list, choose the SINUMERIK 840DT since it is the one used by our EMCO CNC Turning Machine, then click on “start turning” on the right panel. At this stage, MTS TOPTURN will start; (Fig 3.5) Fig. 3.5 MTS TOPTURN Main icons The description of each icon will be displayed by pointing on the icon itself. Open NC Program: to open new or existing NC program. NC Editor: to write or edit an NC program. Setup mode: to make the machine setup (clamping devices, tools … etc). Tool equipment: to choose the tools needed for the different machining operations; this icon will not be activated if you are not in setup mode. Simulation modes: Automatic mode: to run an NC program automatically. Single block mode: to run an NC program block by block where the operator need to confirm the execution of each block. Interactive mode: to run an NC program block by block with the possibility to edit the executed block if not confirmed with the needed operation. Simulation controls: Pause Stop Test run: when clicking on this icon during an NC program run, the simulation goes faster. This has nothing to do when executing the program on the machine. Dimensioning: to check the dimensions of the work part. Graphic modes: 2D Graphic: shows the simulation in 2D. 3D graphic: shows the simulation in 3D. 3D graphic (part): shows the simulation in 3D (work part only) Colorize work piece: gives colors for the different machined sections on the work part Full section: shows a longitudinal section of the work part. Display modes: Reset: gives you 5 preset displays with different overview. Scale up: to zoom in Scale down: to zoom out Zoom rectangle: to zoom in on a selected area Move 3D graphic: to move the 3D graphic up and down, right and left. Study 3D graphic: to rotate the 3D graphic around 3 axes. Example: TOPTURN icons exploration. Open NC program Choose any NC program Click “open” To see the program, Click “editor”.twice. Click on “save and exit” at the top to exit from the program. Click on “setup mode” to activate the tool equipment icon. Click on “tool equipment” to see the tools mounted on the turret (tools magazine). Click on “quit” to exit from the tool equipment. Run the program using “automatic mode” (click on “pause” then resume simulation while running). Run the program using “single block mode” (click on “test run” while running) Run the program using “interactive mode” (switch between “2D graphic”, “3D graphic” or “3D graphic (part)” while running). You can click “stop” at any step while running the program. Use the zoom icons to view specific areas. Click on “Dimensioning” and explore icons to check the dimensions of the work part. 5. Preparing a Setup Form: Tools needed to machine a work part have to be stored in a file or a “setup form”. Starting from the main menu of TOPTURN, the following procedure will describe how to create a set-up form: Click on “setup mode” Click on “tool equipment”. The Turret Equipment window will open; (Fig. 3.6) Fig. 3.6 Turret Equipment The turret equipment window shows the tools mounted in the turret. You can see the characteristics of each tool by selecting it. Click on “File”, then “new” to remove all tools from the turret. Double click on position #1. The “Tools Type Selection” window will open; Fig. 3.7. Fig. 3.7 Tools Type Selection Choose the tool type e.g. “Left Corner Tool” by double clicking on it. Select the required tool e.g. “CL MSBNL – 2020 L 1204 ISO30”; Fig. 3.8. Fig. 3.8 Tool Selection Click on “select and quit” Click on to give a color to the tool, so when it operates, the machined area will have the same color as the tool. If you want to remove a tool, click on “remove” When you finish selecting your tools, click on “Save and quit”. The main window will open and you will see your selected tools, in their positions on the turret; Fig. 3.9 Fig. 3.9 Turret after tool selection Click on “quit” in the bottom menu. Click on “setup form” Click on “generate”. At this stage, the software will ask for a name for this setup form e.g. tool_ex1 Click on “save Click “yes” to create the file. Click on “quit” The setup form now is saved. But when calling this setup form to use it in order to machine the work part, it will not be found in the list of saved setup forms. The software search for setup forms in a folder called “setup-T” for turning and “Setup-M” for milling. That’s why it is necessary to copy the file to the correspondent folder. The procedure is the following: Open NC program; (you have to be in a folder called “SIN840DT” if not, check with your teacher) Search for your file, right-click on it and select “copy” Go two levels up Open “Setup-T” Click “paste” Click “cancel” Now the setup form is saved correctly. 6. Preparing a Setup Sheet In order to set the machine, a setup sheet is created. This is done by clicking on “setup dialog” in the bottom menu. At this stage, the software ask for a name for this program e.g. example_1. By clicking on “open”, the setup sheet preparation procedure begins, where the following has to be mentioned: Chuck device; Fig. 3.10 Chuck‘s type Chuck’s dimensions Chucking depth Fig. 3.10 Chuck device Blank / Zero Point; Fig. 3.11 Blank part’s dimensions Material; Fig. 3.12 (Follow the teacher's instructions) Zero point location Fig. 3.11 Blank / Zero Point Fig. 3.12 Material Selection - Tools; Fig. 3.13. At this stage, you can click on “Select turret equipment” to call the setup form you prepared or use an already saved setup form. “Edit turret equipment” is used to change the tools on the turret. Fig. 3.13 Tools Click “ok” twice. To see your setup sheet, click on “editor”. The following is the automatically generated Setup Sheet: (words in bold are added in this module for explanation) {) Character informing the controller the beginning of the setup sheet {{ 15.04.2008 14:47 Time of last run. This line will not be taken into consideration by the controller because it comes after a double bracket character {{ { All instructions after a one bracket character {are processed by the controller} { CONFIGURATION { MACHINE MTS01 TM-016_-R1_-060x0646x0920 { CONTROL SINUMERIK 840DT { { PART { CYLINDER D+060.000 L+142.000 { MATERIAL "N\Aluminium\AlMg1" { DENSITY 002.70 { { MAIN SPINDLE WITH WORKPART { CHUCK "Chuck Turning\Jaw chuck\KFD-HS 130" { STEP JAW "Jaw\Step jaw\HM-110_130-02.003" { CHUCKING DEPTH E25.000 {{ Right side of the part: Z+235.000 { { TOOLS { T01 "DIN69880 V 30\Left corner tool\CL-SCLCL-2020 L 1208 ISO30" { T02 EMPTY { T03 EMPTY { T04 EMPTY { T05 "DIN69880 V 30\Recessing tool\ER-SGTFL-2012 L 02.0-0 ISO30" { T06 "DIN69880 V 30\Left threading tool\TL-LHTR-2020 R 60 3.50 ISO30" { T07 "DIN69880 V 30\Spotting drill\DR-15.00 034 L HSS ISO30" { T08 EMPTY { T09 "DIN69880 V 30\Twist drill\DR-15.00 067 L HSS ISO30" { T10 EMPTY { T11 EMPTY { T12 EMPTY { T13 EMPTY { T14 EMPTY { T15 EMPTY { T16 EMPTY { { TOOL COMPENSATION Automatically generated calculations allowing the controller to precisely locate the tool tip { D01 T01 Q3 R000.800 X+070.000 Z+045.000 G000.000 E005.005 I-000.800 K-000.800 A+004.375 L011.855 N01 { D02 T02 Q0 R000.000 X+000.000 Z+000.000 G000.000 E000.000 I+000.000 K+000.000 A+000.000 L000.000 N01 { D03 T03 Q0 R000.000 X+000.000 Z+000.000 G000.000 E000.000 I+000.000 K+000.000 A+000.000 L000.000 N01 { D04 T04 Q0 R000.000 X+000.000 Z+000.000 G000.000 E000.000 I+000.000 K+000.000 A+000.000 L000.000 N01 { D05 T05 Q3 R000.200 X+060.000 Z+041.000 G002.000 E000.000 I-000.200 K-000.200 A+000.000 L012.000 N01 { D06 T06 Q8 R000.505 X+070.000 Z+042.699 G000.000 E000.000 I-000.505 K+000.000 A+000.000 L000.000 N01 { D07 T07 Q7 R000.000 X+000.000 Z+106.000 G015.000 E045.000 I+000.000 K+000.000 A+000.000 L000.000 N01 { D08 T08 Q0 R000.000 X+000.000 Z+000.000 G000.000 E000.000 I+000.000 K+000.000 A+000.000 L000.000 N01 { D09 T09 Q7 R000.000 X+000.000 Z+140.000 G015.000 E059.000 I+000.000 K+000.000 A+000.000 L000.000 N01 { D10 T10 Q0 R000.000 X+000.000 Z+000.000 G000.000 E000.000 I+000.000 K+000.000 A+000.000 L000.000 N01 { D11 T11 Q0 R000.000 X+000.000 Z+000.000 G000.000 E000.000 I+000.000 K+000.000 A+000.000 L000.000 N01 { D12 T12 Q0 R000.000 X+000.000 Z+000.000 G000.000 E000.000 I+000.000 K+000.000 A+000.000 L000.000 N01 { D13 T13 Q0 R000.000 X+000.000 Z+000.000 G000.000 E000.000 I+000.000 K+000.000 A+000.000 L000.000 N01 { D14 T14 Q0 R000.000 X+000.000 Z+000.000 G000.000 E000.000 I+000.000 K+000.000 A+000.000 L000.000 N01 { D15 T15 Q0 R000.000 X+000.000 Z+000.000 G000.000 E000.000 I+000.000 K+000.000 A+000.000 L000.000 N01 { D16 T16 Q0 R000.000 X+000.000 Z+000.000 G000.000 E000.000 I+000.000 K+000.000 A+000.000 L000.000 N01 { { WORKPART ZEROPOINTS {{ Right side of the part: Z+235.000 { G54 X000.000 Z+233.000 { {) Character informing the controller the end of the setup sheet Student's Notes: ________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________ ________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________ ________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________ ________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________ ________________________________________________________________________________________________________________________________________________________________________ Practical Tasks Create a setup form having the following tools: Pos. #1: Left Corner Tool, CL-SCLCL 2020 L 1208 ISO30 Pos. #2: Twist Drill, DR-18.00 130 R HSS ISO30 Pos. #3: Spotting drill, DR-15.00 034 L HSS ISO30 Solution: setup mode tool equipment File / New Double click on position 1 Left Corner Tool Select CL-SCLCL 2020 L 1208 ISO30 Click on “select and quit” Repeat steps d through g for tools 2 and 3. Click on “Save and quit”. Quit Setup Form Generate: m3_t1_(your section number), i.e. m3_t1_05 Save Yes Quit Open NC Programs Search for your file Copy Two levels up Search for Setup_T Open Paste Cancel Create a setup sheet having the following parameters: Outside chuck Chuck code: KFD-HS 130 min.10 max.076 Et=33 Chucking depth = 25mm Blank dimensions : Diameter D = 40mm, Length = 80 mm Material : Aluminum Zero point location: left work part side Zero point shift: 2mm right Tools: list created in task #1. Solution: Setup Dialog: m3_t2_(your section number) Open Chuck Device Outside Chuck KFD HS 130 min.10 max.076 Et=33 Chucking Depth = 25 Blank / Zero Point Length L=80 Outer Diameter D=60 Material (Open folder to the right) Non-Ferrous Metals Aluminum Choose the type you want Select and quit Zero point: right workpart side Zero point shift OZ=-2 Tools Select turret equipment Open the drop down list Select m3_t1_(your section number) OK Work Sheet Define CNC. __________________________________________________________________________________________________________________________________________________________________ What is the role of a simulator? __________________________________________________________________________________________________________________________________________________________________ State the advantages of CNC. ______________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________ State the disadvantages of CNC. ____________________________________________________________________________________________________________ ____________________________________________________________________________________________________________ complete the following table: Symbol Description Fill in the blanks: a) The ____________________is used to create NC programs, simulate them and check their quality. ________________is a CAD/CAM system for turning and milling ______________________is used for turning programming, simulation and collision detection. ___________________is one of the CNC machines controllers. ________________________is used to prepare the setup sheet ________________________ run an NC program block by block where the operator needs to confirm the execution of each block. ________________________ run an NC program block by block with the possibility to edit the executed block if not confirmed with the needed operation. 7. Select the suitable chuck to hold a workpiece φ80 X 100 mm and chucking depth of 25 mm : KFD – HS 130 min 10 max 76 Et = 20 KFD – HS 130 min 10 max 100 Et=30 KFD – HS 130 min 81 max 200 Et=80 8. Answer the following questions using the setup sheet below. a)- What is the chucking depth? b)- What is the current tool being used? c)- Where is the workpiece zero point position? d)- How many tools are mounted on the turret? e)- What are the length and the diameter of the workpiece? |

Reference:

1. CNC Basics - MTS